HOF5 Operations Manual
# Opening and Closing the Drain Ports
There are five drain ports on the rig. Their locations are marked on the P&ID.
- Under the feed tank there is a valve that can be opened to drain. A spanner is required to open and close this valve.
- Upstream of PP01 there is an RJT connection with a blanking plate.
- Under the membrane inlet manifold there is an RJT connection with a blanking plate.
- Under the lower permeate manifold there is a manual isolation valve with a black handle.
- Under the permeate tank there is a manual isolation valve with a red handle.
A C-Spanner is required for the RJT connections.
# Production
1. Ensure all drains are closed, as per the instructions above.
2. Set the swing bend such that permeate is not returned to the feed tank. Connect to permeate discharge via the swing bend to ensure it remains connected to the plant and is not lost.
3. Connect feed via V63.
4. Connect Retentate Bleed (if desired).
5. Connect Retentate Out to RJT connection at V62.
6. Select production on the Operation switch.
7. Select appropriate membrane on the Membrane Type switch (stainless steel or polysulfone).
8. Press the Reset button to clear the fault warning light if it is lit—once the reasons for a fault have been explored.
9. Press the Start button.
- If the concentrate button is not pressed, V63 will open, admitting feed to feed tank. If the concentrate button is pressed during production, V63 will close and remain closed. The concentrate button can be pressed at any time during production.
- When sufficient liquid is in the feed tank, circulation will start.
- Process includes back-flushing of membranes at regular intervals using produced permeate and pumping of permeate when there is sufficient in the tank.
1. When sufficient permeate has been produced the permeate will be discharged from V17.
2. Press the Stop button to end production.
Manual back-flush of the membrane modules can be initiated by pressing the back-flush button during production.
Manual discharge of permeate from the permeate tank and retentate from the feed tank can be initiated by pressing the appropriate button but only when the plant is stopped, see the instructions below.
# Emptying the Feed Tank
1. Press the Stop button to ensure the machine has come to a halt.
2. Press the Reset button to clear the fault warning light if it is lit—once the reasons for a fault have been explored.
3. The position of the operation and membrane type switches are not important; they can stay as they are.
4. Press the Retentate Out button.
  - V62 will open and V61 will close
  - Retentate will be pumped by PP01 until the feed tank is empty (as checked by LT02 and then a timer runs the pump once the tank level is below that which the level transmitter can detect).
  - Retentate will flow via V62.
The feed tank, or retentate tank, can be emptied only when the machine has stopped.
# Emptying the Permeate Tank
1. Press the Stop button to ensure the machine has come to a halt.
2. Press the Reset button to clear the fault warning light if it is lit—once the reasons for a fault have been explored.
3. The position of the operation and membrane type switches are not important; they can stay as they are.
4. Press the Permeate Out button.
  - V17 will open
  - Permeate will be pumped by PP02 until the permeate tank is empty (as checked by LT01 and then a timer runs the pump once the tank level is below that which the level transmitter can detect).
  - If the swing bend is in place, permeate will be pumped back into the feed tank. Otherwise, permeate will flow via V17.
The permeate tank can be emptied only when the machine has stopped.
# Emptying the Rig
For cleaning or for transport the rig may be emptied by:
1. Empty the feed tank, as per the instructions above.
2. Empty the permeate tank, as per the instructions above.
3. Open the drain valves, as per the instructions above.
4. Allow the retentate to drain from the upper retentate manifold down through the membrane modules and out the drain of the membrane inlet manifold.
5. Once the rig is emptied, close all the drains that were opened.
# Cleaning the Rig
1. Fit the swing-bend from V17 such the permeate tank will discharge to the feed tank.
  Rinse
2. Empty the rig, as per the instructions above.
3. Add 200L of water at 50°C to the feed tank. The polysulfone membranes typically have a maximum cleaning temperature of 54°C[1].
  [1] See http://kochmembrane.com/PDFs/Data-Sheets/Hollow-Fiber/UF/romicon-5-inch-hf-ctg-general-datasheet.aspx
4. Press the Reset button to clear the fault warning light if it is lit—once the reasons for a fault have been explored.
5. Set the operation switch to CIP.
6. Press the Start button
- PP01 will circulate the water around the rig.
- V63 (the feed tank inlet valve) will remain closed.
- The membranes will automatically be regularly backwashed.
- The rig will automatically stop after 15 minutes.
Alkali Wash
1. Empty the rig, as per the instructions above.
2. Add 200L of water at 50°C to the feed tank and sufficient Ultrasil 91 to bring the pH to 11.5 to 12.0. The polysulfone membranes typically have a maximum allowable pH of 13 with a solution temperature of 54°C1.
3. Press the Reset button to clear the fault warning light if it is lit—once the reasons for a fault have been explored.
4. Press the Start button
  Rinse
5. Rinse the plant as above, probably twice, until a pH of less than 8.5 is obtained.
  Acid Wash
6. Empty the rig, as per the instructions above.
7. Add 200L of water at 50°C to the feed tank and sufficient Ultrasil 75 to bring the pH down to 2.5 to 3.0. The polysulfone membranes typically have a minimum allowable pH of 1.5 with a solution temperature of 54°C1.
  Rinse
8. Rinse the plant as above, probably twice, until a pH of at least than 6.0 is obtained.
9. The rig is now clean.