HOF5 Operations Manual
# Production Procedure

1. Ensure all drains are closed.
2. Set the swing bend such that permeate is not returned to the feed tank. Connect to permeate discharge via the swing bend to ensure it remains connected to the plant and is not lost.
3. Connect feed to V63.
4. Connect Retentate Bleed (if desired).
5. Connect Retentate Out to RJT at V62.
6. Select production on the operation switch.
7. Select appropriate membrane on the membrane type switch (stainless steel or polysolphone).
8. Press the Reset button to clear the fault warning light, once the reasons for a fault have been explored.
9. Press the Start button.
- V63 will open admitting feed to feed tank.
- When sufficient liquid is in feed tank circulation will start.
- Process includes back-flushing of membranes at regular intervals using produced permeate and pumping of permeate when there is sufficient in the tank.

1. When sufficient permeate has been produced the permeate will be discharged from V17.
2. Manual back-flush can be initiated by pressing the back-flush button during production.

Manual discharge of permeate from permeate tank and/or retentate from the feed tank by pressing the appropriate button only when the plant is stopped.